## Slide 1: Harmonic Control Arrays
Murat DOĞRUEL
Marmara University, Faculty of Engineering
mdogruel@marmara.edu.tr

## Slide 2: Outline
“Harmonic Control Arrays” method is introduced.
An example is provided to demonstrate how it works.
The results and the future work are summarized.

## Slide 3: Motivation
u
For constant references, the steady state error can be automatically eliminated by simply utilizing an integral term in unitary feedback systems. This is frequently and very usefully employed in many industrial control solutions.
y
-
Controller
r
e
+
Plant
+

## Slide 4: Motivation
u
How can we achieve the zero error performance for systems containing periodic references and/or periodic disturbances?
y
-
Controller
r
e
+
Signal
Producer
+
Plant

## Slide 5: An Illustration of the HCA Idea
Input
Signal
Dispersed
Signal
HCA
Modified
Dispersed
Signal
Output
Signal
Each harmonic component is individually controlled to construct the output.

## Slide 6: The HCA Method
The method is based on automatically constructing the appropriate control signal by adjusting the complex levels of its harmonic components, using the harmonic components of the reference and output signals.

## Slide 7: Harmonic Control Arrays Block Diagram
<y>
u
< >
HCA
> <
< >
r
<r>
<u>
y
llhllh
Plant

## Slide 8: Harmonic Disperser
< >
x
<x>

## Slide 9: Harmonic Assembler
> <
<x>
x

## Slide 10: Harmonic Control Arrays
The HCA block tries to “optimally” construct <u>
using <r> and <y> (and their previous values).
y
<y>
u
< >
HCA
> <
< >
r
<r>
<u>

## Slide 11: Harmonic PI Control Array
y
-
< >
> <
r
<e>
<u>
u
e
+
+

## Slide 12: A Sample Application
A typical plant model
u
y
+
d

## Slide 13: The reference and disturbance signals
<r> = [2.7; -1; 0.5j; 0.2; -0.1j],
<d> = [0.35; -1.6+1.6j; 0.25-0.3j; -2.95+3.05j; 2.5+1.25j].
0
1
2
3
4
5
-2
0
2
4
6
r(t) Reference Input
0
1
2
3
4
5
-20
-10
0
10
20
d(t) Disturbance
t (sec)

## Slide 14: The system without delay
a = 1, T = 1, Td = 0,
KP = diag([2.5; 10; 15; 20; 20]),
KI = diag([0.9; 4; 10; 10; 10]).
0
5
10
15
-4
-2
0
2
4
6
8
The Reference and the Output
0
5
10
15
-4
-2
0
2
4
6
t (sec)
The Error
r(t)
y(t)
e(t)
t (sec)

## Slide 15: The Dispersion of the Output Signal
0
5
10
15
-2
-1
0
1
2
3
4
The Real Parts of <y>
t (sec)
h=0 -> 2.7
h=1 -> -1
h=2 -> 0
h=3 -> 0.2
h=4 -> 0
0
5
10
15
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
1.4
The Imaginary Parts of <y>
t (sec)
h=0 -> 0
h=1 -> 0
h=2 -> 0.5
h=3 -> 0
h=4 -> -0.1

## Slide 16: The Composed Control Signal
0
5
10
15
-40
-20
0
20
40
60
u(t)
t (sec)

## Slide 17: The System with Delay (Td =0.1 sec.)
0
5
10
15
-2
0
2
4
6
The Reference and the Output
0
5
10
15
-2
0
2
4
6
t (sec)
The Error
r(t)
y(t)
e(t)
KP = diag([1.1; 0.4+1.4j; 0; -8-6j; 1.5-4.7j]),
KI = diag([0.9; 1.5+4.7j; -10+7j; -12-9j; 5-14j]).
t (sec)

## Slide 18: The Behavior for a Constant Reference
<r> = [10; 0; 0; 0; 0].
0
5
10
15
-5
0
5
10
15
The Reference and the Output
t (sec)
r(t)
y(t)
0
5
10
15
-10
0
10
20
30
The Composed Control Signal
t (sec)

## Slide 19: The Robustness of HCA
0
5
10
15
-2
0
2
4
6
t (sn.)
The Error
a = 1
a = 0.7
a = 1.3

## Slide 20: The Unstable System with Delay
a = -1, Td = 0.1,
KP = diag([-1.65; 3; 0; 0; 10]),
KI = diag([-0.3; 7; 5; 10; 15]).
The Reference and the Output
The Error
0
5
10
15
-5
0
5
10
0
5
10
15
-5
0
5
10
t (sec.)
r(t)
y(t)
u
y
+
d
t (sec.)

## Slide 21: A Periodic Position Control Example
M
Motor
Driver
Data Acq.& Control
Position Encoder
Load
M
Linear motion mechanism
u
y
Host PC
Total RMS Errors in One Period |  |  | 
Method | No load | Symmetric load | Asymmetric load
PI | 0.8453 | 1.4753 | 1.2684
PI+IMC | 0.0716 | 0.1327 | 0.1037
HCA (H=2) | 0.0658 | 0.1139 | 0.0863
HCA (H=3) | 0.0528 | 0.0867 | 0.0696
HCA ( H=4) | 0.0434 | 0.0650 | 0.0545

## Slide 22: Conclusions - 1
The method of “Harmonic Control Arrays ” is introduced.
HCA method offers an effective control solution for systems with periodic references and/or disturbances having a certain number of harmonic components.
The HCA method achieves the zero error by automatically producing the control signal, composed of the harmonic components at correct magnitudes and phases.
This kind of solution is frequently needed and directly applicable for industrial control problems.

## Slide 23: Conclusions - 2
The algorithm can be easily and flexibly implemented on a microcontroller or a digital signal processor as a prototype control solution. Then, the control engineer just need to adjust the PI complex gain matrices for the Harmonic PI Control Array Method.
As seen from the examples, despite the delay and disturbance, a fast and robust performance can be achieved.
The HCA method allows the famous PID control to be effectively and easily adapted to the systems involving periodic signals.

## Slide 24: Future Work
To further develop this method, theoretical investigations about stability and control design should be carried out, and it should be tested on real applications.
The other control methods can also be utilized in implementing harmonic control arrays, and HCA can be used in parallel with the other methods.
HCA look promising for many industrial applications like control of DC/AC or AC/DC converters as well as noise cancellation type problems.

## Slide 25: Thank You. Any Questions?
Input
Signal
Dispersed
Signal
HCA
Modified
Dispersed
Signal
Output
Signal
http://www.rit.edu/~andpph/photofile-c/prism-DSCN5003.jpg